Explicit Congestion Notification (ECN)

CISC 856: TCP/IP & Upper Layer Protocols

Qi (Gill) Wang (gillwang@udel.edu)

Due date: Dec 11, 2012

Part – 1

Please refer to RFC 3168 if needed.

- Why is the ECN field maintained in the regular header of an IP-PDU rather than as an IP option?

- Explain why the TCP data receiver SHOULD ignore the ECN field on arriving data PDUs that are outside of the receiver’s current window.

- Describe the procedure of ECN negotiation in the TCP Initialization.  Explain why a host must not set ECT in the IP-PCI of SYN or SYN-ACK TCP-PDUs.

- Recall that one of the ICMP error reporting messages, i.e., source quench also notifies the end hosts when a router experiences congestion. Source quench is quicker in notifying the sender of congestion compared to the ECN mechanism. Then, is source quench a better notification mechanism than ECN? Why or why not?

- What will happen if a TCP-PDU with CWR set gets lost?

Part –  2 Wireshark

In this part, we are going to see how the source and destination exchange information about their willing to use ECN in TCP Initialization.

Step 1 Many operating systems, such as Windows 7, Mac OS X 10.5, Linux 2.6, have support for ECN; however, ECN is disabled by default. Enable ECN in your computer.

Step 2 Start up the Wireshark software and begin packet capture.

Step 3 Start up your web browser. Enter the URL http://www.ucla.edu and have that page displayed in your browser.

Step 4 Stop Wireshark packet capture.

Questions:

- Describe how to enable ECN in the operating system of your computer?

- Print out the TCP Initialization PDUs with ECN negotiation. Annotate the ECN flags and indicate the willingness of your computer and the webserver to use ECN.

- Print out an ECN-capable PDU. Annotate the ECN flags.