## Slide 1: Explicit Congestion Notification (ECN)
Qi (Gill) Wang
gillwang@udel.edu
CISC 856 – TCP/IP, Fall 2012
Special thanks to:
Dr. Paul Amer
Guna Ranjan, Justin Yackoski, Namratha Hundigopal and Preethi Natarajan for slides

## Slide 2: Overview
Congestion control
  TCP congestion control
  Active Queue Management (AQM)
  Explicit Congestion Notification (ECN)
ECN in IP and TCP
Example
Advantages and implementations

## Slide 3: Congestion
Routers have buffers that hold the packets before and after processing
Buffers are finite, so it is possible for more packets to arrive at a router than the router can buffer
    The router becomes overloaded, and congestion occurs
Typical effects of congestion
  Queue delay
  Packet loss
  Blocking of new connections
Sender
Receiver
Packets are dropped

## Slide 4: TCP Congestion Control
TCP
  Treats the network as a “black-box”
  Relies on packet loss as the indication of congestion
Congestion detection
  Three duplicate ACKs
  RTO timer times out
Congestion avoidance
  Multiplicative decrease
  Reaction after congestion has already happened!
  Congestion has already happened!

## Slide 5: Drawbacks of TCP Congestion Control
Not helpful for delay-sensitive flows
  The increased latency of the packet is caused by the need to retransmit the packet after a loss
Sender 4
Sender 3
Sender 2
Sender 1
Undesirable global synchronization
  All flows reduce the sending rate simultaneously  channel is under-utilized
  All flows start retransmission/increasing the sending rate in a similar fashion  congestion occurs again
Lockout
  The shared resource is unfairly consumed exclusively by a small number of flows
  The remaining flows are denied access to the resource
x
x

## Slide 6: Active Queue Management (AQM)
Routers detect congestion before the buffer is full
  Incipient congestion indicated by the average queue size
The router provides an indication to the hosts before congestion loss really happens
  Mark packets  ECN
Sender
Receiver
thmin
thmax

## Slide 7: Explicit Congestion Notification (ECN)
ECN is an AQM mechanism
Sender responds to ECN indication the same as to a packet drop
  Halve cwnd
Support from two layers
  Network layer: signaling between routers and hosts
    IP
  Transport layer: host-to-host signaling, congestion control
    TCP, SCTP

## Slide 8: ECN Bits in IP Header
Differentiated Services Codepoints 6 bits | Unused 2 bits
VER 4 bits | HLEN 4 bits | DS 8 bits | Total Length 16 bits | 
Identification 16 bits |  |  | Flags 3 bits | Fragmentation offset 13 bits
Time to Live 8 bits |  | Protocol 8 bits | Header Checksum 16 bits | 
Source IP Address 32 bits |  |  |  | 
Destination IP Address 32 bits |  |  |  | 
Options (if any) |  |  |  | 
Differentiated Services Codepoints 6 bits | ECT 1 bit | CE 1 bit
ECT: ECN Capable Transport
CE: Congestion Experienced
ECT | CE | 
0 | 0 | Not-ECT
0 | 1 | ECT (1)
1 | 0 | ECT (0)
1 | 1 | CE

## Slide 9: ECN Bits in TCP Header
Source port address 16 bits |  |  |  |  |  |  |  | Destination port address 16 bits
Sequence Number 32 bits |  |  |  |  |  |  |  | 
Acknowledgement Number 32 bits |  |  |  |  |  |  |  | 
HLEN 4 bits | Reserved 6 bits | U R G | A C K | P S H | R S T | S Y N | F I N | Window size 16 bits
Checksum 16 bits |  |  |  |  |  |  |  | Urgent pointer 16 bits
Options (if any) |  |  |  |  |  |  |  | 
Reserved (6 bits) | URG | ACK | PSH | RST | SYN | FIN
Reserved (4 bits) | CWR | ECE | URG | ACK | PSH | RST | SYN | FIN
CWR: Congestion Window Reduced
Set after TCP sender has reacted to ECN
ECE: ECN-Echo
 Set when TCP receiver wants to inform the sender of congestion

## Slide 10: ECN Negotiation in TCP
TCP Sender
TCP Receiver
ECN-Setup SYN
CWR = 1
ECE = 1
SYN = 1
ECN-Setup SYN-ACK
CWR = 0
ECE = 1
ACK = 1
SYN = 1
ACK
ACK = 1

## Slide 11: Example
Incipient congestion detected.
If ECT, then set CE.
ECN-Capable sender
ECN-Capable router
ECN-Capable receiver
ECN capability negotiated during TCP connection establishment
ECT | 
IP | TCP
Congestion!!
TCP sender halves
cwnd and sets CWR in
TCP-PCI.
Congestion!!
IP receiver tells TCP receiver.
TCP receiver informs TCP sender.
Sender has reduced cwnd,
TCP receiver stops ECE flag
CWR | 
IP | TCP
CWR | 
IP | TCP
CE | 
IP | TCP
ECE | 
IP | TCP
IP | TCP
ECE | 
IP | TCP
IP | TCP
ECT | ECN Capable Transport
CE | Congestion Experienced
CWR | Congestion Window Reduced
ECE | ECN-Echo

## Slide 12: Rules
No ECT set on SYN, SYN-ACK or “pure” ACK PDUs
No ECT set unless one ECN-setup SNY or ECN-setup SYN-ACK PDUs has been sent and received
No ECT set for retransmitted PDUs
Keep the same ECN flags in reassembly when all fragments carry the same ECN set
In TIME-WAIT or CLOSE sate, hosts ignore any ECN signaling for that connection
…

## Slide 13: Advantages of ECN
Feedback to the TCP sender before the router drops packets
Less retransmission
Improve throughput and goodput of the whole internetwork

## Slide 14: Implementations
ECN support in TCP by hosts
  Windows 7, Mac OS X 10.5, Linux 2.6, others?
  Many modern implementations of the TCP/IP protocol suite have support for ECN; however, ECN is disabled by default
ECN support in IP by routers
  Cisco IOS routers with IOS Release 12.2(8)T, others?

## Slide 15: Summary
Incipient congestion is detected
Routers are no longer limited to packet drops as an indication of congestion
ECT and CE flags are used in IP-PCI for signaling between routers and hosts
ECN-Echo and CWR flags are used in TCP-PCI for host-to-host signaling

## Slide 16: Reference
RFC 3168 – The Addition of Explicit Congestion Notification (ECN) to IP
RFC 2309 – Active Queue Management
http://en.wikipedia.org/wiki/Explicit_Congestion_Notification#Implementations
http://en.wikipedia.org/wiki/Network_congestion#Active_Queue_Management_.28AQM.29
Slides from Guna Ranjan, Justin Yackoski, Namratha Hundigopal and Preethi Natarajan
R. Kinicki and Z. Zheng, “A Performance Study of Explicit Congestion Notification (ECN) with Heterogeneous TCP Flows,” http://web.cs.wpi.edu/~rek/ICN01talk.ppt

## Slide 17: Q & A
Thanks!

## Slide 18: AQM Router Mechanism
1
0
Average Queue Length
Min-threshold
Max-threshold
Dropping/Marking Probability
Queue Size
max_p

## Slide 19: ECN Goodput Improvement
  RED: an AQM technique indicating congestion by packet drops
  ECN performs better